## Slide 1
ICAI | 21 June 2026
Development Control
Regulations (DCR)
& Real Estate Compliance
Role of Chartered Accountants in DCR Certification & Audit
CA Ramesh Prabhu, CEO, Viksit Consulting. 9820106766/68 / rameshprabhu@viksitconsulting.com
Notes: Welcome everyone. Today we discuss Development Control Regulations — what they are, how they govern real estate, and crucially, the role of the Chartered Accountant in DCR compliance, certification and audit. This is a 1-hour session covering both the regulatory framework and practical implications for our profession.

## Slide 2
Session Agenda
1
Purpose & Structure of DCR / Zonal Regulations
2
Land Use Classification & Zoning Norms
3
FSI / FAR, Setbacks, Coverage & Height Restrictions
4
Building Approval Process: Layout, Sanction & Deviation
5
Transferable Development Rights (TDR) — Accounting & Tax
6
Regularisation of Deviations: Procedures & Consequences
7
DCR Compliance under Section 11 of RERA
8
Legal Role of CA in Certification of Compliance
9
Common Irregularities in Project Audits
10
Case Study: DCR Violations → RERA Penalties
Notes: This is the roadmap for our session. We cover 10 interconnected topics — from the basic framework of DCR to the very practical question of what a CA must do when certifying compliance. Case study at the end ties everything together.

## Slide 3
What is DCR? Purpose & Structure
DCR — Defined
Development Control Regulations
are statutory rules framed by urban local bodies (ULBs) / planning authorities under the Maharashtra Regional & Town Planning Act, 1966 (MRTP Act). They regulate:
→ What can be built
→ Where it can be built
→ How much can be built
→ How it must be built
Key Regulatory Bodies
MCGM / BMC
Mumbai — DCPR 2034
MMRDA
Metro Region Development Plan
MahaRERA
RERA-linked compliance
Town Planning Dept.
Zonal Regulations
UDCPR 2020
Unified DCR for entire Maharashtra
Key Insight: DCR is the Constitution of real estate development — everything starts and ends here.
Notes: DCR is the foundational legal framework for all construction activity. In Maharashtra, DCPR 2034 governs Mumbai. The Unified DCPR 2020 extends similar regulations to the rest of Maharashtra. Everything from floor space to building height, from setbacks to amenity spaces — all regulated under DCR. As CAs, we encounter DCR compliance in RERA project certifications, audit reports, and deviation regularisations.

## Slide 4
Land Use Classification & Zoning Norms
Residential (R)
R1, R2, R3 zones — permissible uses, FSI, tenement density, permissible commercial uses on ground floor
Commercial (C)
Office, retail, hotels, malls — higher FSI, parking norms, fire safety requirements
Mixed Use (M)
Residential + commercial permissible. DCPR 2034 expanded mixed-use corridors along arterial roads
Industrial (I)
Manufacturing, warehousing. Conversion / redevelopment requires zone-change approval from competent authority
Green / No Dev.
Natural zones, CRZ, reserved plots, eco-sensitive areas — no or restricted construction
Public Semi-Public
Schools, hospitals, govt. offices — specific FSI concessions and amenity-space obligations
CA Note: Zone classification determines FSI, permissible usage & TDR eligibility — verify before certifying project compliance.
Notes: Zoning determines what category of land use is permitted. Before any project certification, a CA must verify the zone in the Development Plan (DP). A developer cannot construct residential flats in an industrial zone without a formal zone change. MahaRERA requires the zoning certificate to be uploaded. Errors here lead to project registration rejection or later cancellation.

## Slide 5
FSI / FAR, Setbacks, Coverage & Height Restrictions
FSI = Floor Space Index
Total Built-up Area
────────────────
Plot Area
(Also called FAR — Floor Area Ratio)
Types of FSI in DCPR 2034
Base FSI
1.0 to 1.33 (residential, Mumbai)
Premium FSI
Additional FSI on payment to ULB
TDR FSI
Transferable Development Rights
Fungible FSI
Upto 35% extra (balconies, utilities)
Ancillary FSI
Staircases, lift, common areas
Ground Coverage
Max % of plot that can be covered by building footprint (typically 50-75%)
Setbacks
Minimum open space required on all sides of building — front, side, rear
Height Restrictions
AAI / DGCA clearance for airport proximity; Fire NOC for high-rises; ToD zones
⚠ CA Alert: Excess FSI consumption = DCR violation = RERA non-disclosure risk. The CA certifying Form 3 / Form 4 must verify sanctioned FSI vs. actual FSI consumed from the approved plan and OC documents.
Notes: FSI is the single most critical parameter in real estate. A developer who consumes more FSI than sanctioned has violated DCR. CAs must check the sanctioned plan FSI, add TDR and Premium FSI components, and verify against actual built-up area. The Form 3 Architect Certificate cross-checks this, and the CA certificate for MahaRERA must be consistent with it.

## Slide 6
Building Approval Process
1
Layout Plan
Approval
2
IOD
(Intimation of Disapproval)
3
Commencement
Certificate
4
Sanction Plan /
Revised Plan
5
Part / Full OC
(Occupancy Certificate)
Sub-division / amalgamation of plots. Approved by ULB / Planning Authority. Pre-condition for IOD.
Building permit. Issued by BMC/ULB. Specifies FSI, setbacks, land use. Valid 5 years.
Permission to start construction at plinth level after paying premiums and fulfilling IOD conditions.
Any design changes require revised sanction. Deviations without sanction = violation.
After construction per plan. Issued by BMC/ULB. Required for possession, registration & RERA closure.
Deviation Management
Structural Deviations: Changes to RCC frame, additional floors — require fresh sanction + revised IOD. Non-Structural: Internal partition changes — generally condoned.
For RERA: Any deviation >3% of carpet area requires allottee consent (Section 14). CA auditing Form 5 must cross-check approved plan vs. actual.
Notes: The building approval process is sequential and each stage is a legal milestone. IOD = building permit. OC = completion certificate. MahaRERA requires both the IOD and OC (or Part OC) to be uploaded. A CA doing a RERA audit must verify that the OC matches the type — Full OC vs Part OC — as the status of the RERA project depends on this. Deviations from sanctioned plan without revised sanction = Section 14 RERA violation.

## Slide 7
Transferable Development Rights (TDR) — Accounting & Tax
What is TDR?
TDR is a certificate issued by the Planning Authority when land is surrendered/acquired for public purposes (road widening, DP reservations). The land owner receives a DRC (Development Rights Certificate) allowing equivalent FSI to be used on other land within the same zone or adjoining zones. TDR is freely tradeable in the market.
Types of TDR
▸ Road/Slum TDR — surrendered DP reservation land
▸ Heritage TDR — heritage building preservation
▸ Slum Rehabilitation TDR — SRA projects
▸ Amenity TDR — amenity spaces for ULB
▸ In-situ FSI — used on same plot (special cases)
Accounting Treatment
▸ TDR acquired: Intangible Asset (Ind AS 38)
▸ Carried at cost less impairment
▸ On utilisation: transferred to WIP/Project Cost
▸ DRC held for sale: Inventory (Ind AS 2)
▸ Disclosure required: quantum of TDR held & used
Tax Implications
▸ Sale of DRC: Capital Gains (LTCG/STCG)
▸ Indexation benefit if held >24 months (from FY 2024-25)
▸ GST: 18% on DRC sale (SAC 9972 / 9983)
▸ For developers: Deductible as project cost
▸ Section 56(2)(x): Gift of TDR — FMV taxation
Notes: TDR is a significant balance sheet item for real estate developers. As CAs, we must ensure correct classification — intangible asset vs inventory depending on intended use. Taxation is complex: the DRC holder's sale is capital gains, but the developer using it in a project books it as project cost. GST at 18% on DRC sale is often missed. Also watch out for Section 56(2)(x) where a related party gifts TDR below market value.

## Slide 8
Regularisation of Deviations: Procedures & Legal Consequences
Regularisation Process
Step 1
Deviation Survey Report by licensed architect / structural engineer
Step 2
Application to ULB/BMC with as-built drawings and description of deviations
Step 3
Payment of Compounding Fee / Penalty (calculated on excess built-up area)
Step 4
Revised OC issued (if regularisation approved)
Step 5
Update MahaRERA project — upload revised OC, revised plans
Legal & Financial Consequences
Civil
• Demolition / Stop Work Notice
• BMC sealing of property
• Cannot obtain OC → No possession
• Title defect — unmarketable property
RERA
• Delay in project completion → Penalty u/s 12
• Allottees entitled to refund (Section 18)
• CA certificate becomes false/misleading
• MahaRERA may cancel registration
Criminal
• MRTP Act Section 52: Imprisonment up to 3 yrs
• Fine up to ₹5,000 per day of continuance
Notes: Regularisation is not automatic — it is a discretionary approval. The developer must prove the deviation is compoundable under DCR. Many deviations like extra floors are not compoundable and result in demolition orders. For CAs: if your RERA audit reveals an unregularised deviation, you cannot certify Form 5 (completion certificate) without noting it. Your certification must be accurate — a false certificate attracts professional liability.

## Slide 9
DCR Compliance under Section 11 of RERA
Section 11 RERA — Promoter's Obligations at the Time of Registration
Section 11(3): Promoter shall not make any alterations or additions to approved and sanctioned plans without written consent of allottees AND prior approval of competent authority. DCR compliance is thus embedded in RERA's legal architecture.
Disclosure — Section 11(1)
Upload layout plan, FSI details, sanctioned plan on MahaRERA portal at time of registration
Adherence — Section 11(3)
No structural changes without allottee consent + authority approval. Any DCR deviation = RERA violation
Reporting — Section 11(4)
Quarterly updates on project progress including construction milestones per approved plan
Completion — Section 11(4)(b)
Complete project as per sanctioned plan. Issue OC and handover per DCR compliance
Title Disclosure — Rule 3
Encumbrances, liens, zone details must be disclosed upfront — DCR zone-change pending = must disclose
CA Certification
Independent CA certifies financials + architect certifies DCR compliance. Both Form 3 & CA Form must align
DCR non-compliance ≡ RERA non-compliance. One triggers the other automatically.
Notes: Section 11 is the heart of promoter obligations under RERA. The sanctioned plan as per DCR forms the benchmark. Any deviation from it is simultaneously a DCR violation and a RERA violation. As CAs certifying RERA accounts, we must co-read the architect's Form 3 certificate. If the architect notes a deviation, our financial certification cannot ignore it — we have a professional duty to report or qualify.

## Slide 10
Legal Role of CA in DCR Certification of Compliance
Form 3
Architect/Engineer
Structural compliance certificate — certifies DCR adherence, FSI consumed, setbacks maintained
Form 4
CA / Cost Accountant
Architect certificate endorsement + financial audit of project accounts (70% rule compliance)
Form 5
CA + Architect
Completion Certificate — both must certify project is complete per sanctioned plan before OC application
CA's DCR Compliance Checklist
Verify zone classification from DP / Zonal plan
Confirm total FSI sanctioned = Base + Premium + TDR components
Check IOD conditions — are all pre-commencement conditions met?
Trace OC (Full/Part) — match to RERA project status
Review deviation report (if any) from architect
Cross-check 70% escrow utilisation for construction milestones
For Deviation Report CA certificate: verify plan vs. actual built areas
Notes: The CA's role in RERA is not just financial — it intersects with DCR compliance because Form 4 requires us to certify that the project accounts reflect construction progress per the sanctioned plan. The 70% escrow rule ties money to construction — and construction must be per DCR. A CA who blindly certifies without checking DCR compliance takes significant professional risk. Use the checklist on this slide as your standard operating procedure.

## Slide 11
Common Irregularities in Project Audits & Certifications
HIGH
Excess FSI Consumption
Actual built-up area exceeds sanctioned FSI. Often discovered post-construction. Results in non-issuance of OC.
HIGH
OC Mismatch
Part OC uploaded on RERA for a fully occupied building. RERA shows project as 'ongoing' — misleads allottees.
MED
Basement Misuse
Basement sanctioned as parking converted to commercial use. Compounding fee may not be available.
HIGH
Setback Violation
Construction in mandatory open space area. Results in demolition notices, not compoundable in many cases.
HIGH
Unauthorised Floors
Extra floors constructed beyond IOD. Often seen in redevelopment projects where developer adds units.
MED
TDR Double Counting
Same TDR used across multiple wings/buildings. Accounting fraud — each DRC has a unique number and FSI quantum.
Notes: These are real-world irregularities that CAs encounter in RERA audits. Excess FSI and setback violations are most common. OC mismatch is a systemic problem in Maharashtra where Part OC buildings are shown as complete on RERA. TDR double counting is a financial fraud — DRCs have unique certificate numbers and FSI quantum, so cross-check every component. Our professional responsibility requires us to flag these, not overlook them.

## Slide 12
Case Study: DCR Violations → RERA Penalties / Cancellation
CASE SCENARIO
A residential developer in Thane constructs 2 additional floors beyond the sanctioned IOD consuming 18% excess FSI. Project registered on MahaRERA showing Full OC (incorrectly — only Part OC exists). The CA certifies Form 4 without cross-checking the FSI statement. Allottees file complaint after BMC issues Stop Work Notice.
DCR Consequence
▸ BMC issues demolition notice for excess 2 floors
▸ Stop Work Notice — project halted
▸ Compounding fee: ₹8,200/sq.mt × excess BUA
▸ Developer challenges → High Court — years of litigation
RERA Consequence
▸ MahaRERA suo moto takes cognizance
▸ False OC declaration → ₹10 lakh penalty
▸ Project registration suspended
▸ Allottees entitled to refund u/s 18 with interest
CA's Liability
▸ CA who certified Form 4 faces disciplinary action
▸ ICAI complaint for professional misconduct
▸ Civil suit by allottees for negligent certification
▸ Lesson: Always verify FSI statement independently
Notes: This case illustrates how a single DCR violation cascades into RERA penalties and CA liability. The CA here failed to independently verify the FSI statement. The golden rule: never rely solely on the developer's representation. Pull the IOD, check the sanctioned FSI components, and verify the OC type from the original document. Your signature on a RERA certificate is your professional reputation.

## Slide 13
Key Takeaways for CA Practitioners
01
DCR is the foundation — understand the zone, FSI components, and IOD before certifying any RERA document.
02
FSI statement must be independently verified — cross-check Base FSI + TDR + Premium FSI against sanctioned IOD.
03
OC verification is non-negotiable — distinguish Full OC vs Part OC; never rely on developer's oral representation.
04
Deviations must be disclosed — if architect notes deviation, qualify your certificate accordingly.
05
TDR accounting must be correct — intangible asset vs. inventory classification has P&L and balance sheet implications.
06
CA liability in RERA is real — false certification exposes you to ICAI disciplinary action, civil suits, and regulatory penalties.
Notes: Summarise these 6 key messages. The common thread: a CA involved in RERA work cannot be a passive certifier. You need to understand DCR at a practical level. The forms — Form 3, 4 and 5 — are interconnected. Your certification is a legal document and carries professional accountability. Thank your audience and move to Q&A.

## Slide 14
Thank You
Questions & Discussion
DCR (Development Control Regulations) & Real Estate Compliance
CA Ramesh Prabhu, CEO, Viksit Consulting. 9820106766/68 / rameshprabhu@viksitconsulting.com
ICAI — 21 June 2026
Notes: Open to questions. Common questions to prepare for: (1) What if IOD is expired — can RERA registration continue? (2) Is TDR cost included in carpet area cost for allottees? (3) What is the CA's liability if the architect gives a wrong FSI certificate and I certify based on it? Be ready with answers: (1) Expired IOD must be renewed before construction; RERA registration continues but OC cannot be obtained without fresh IOD. (2) TDR cost is a project cost — recoverable from allottees per agreement. (3) CA must apply professional scepticism — over-reliance on another professional's certificate without basic verification is still negligence.